One West Otterson Street, Nashua, New Hampshire 03060.  Ph: (603)883-7979  Fax: (603)883-3266    Email: sales@cepoint.com Website: http://www.cepoint.com

Enterprise & Mission-Critical Serial Attached-SCSI (SAS) RAID System

R-STOR  200 series, compact, rugged, reliable and high performance at work!

| R-STOR™ Serial Attached SCSI systems supporting RAID 0, 1, 5, 6, 10, 50, JBOD and the Adaptec Advanced Data Protection Suite with RAID 1E, 5EE, 6, 60, Copy back Hot Spare and optional Snap shot Backup for pedestal and high-density rack-mount environments needing high storage |
| --- |
| Benefits | High-performance storage connectivity and data protection for servers and workstations |  |
| Customer Applications | RS-200 SAS series RAID storage is Ideal for supporting server and workgroup applications where high levels of sustained read and write operations are required, such as video streaming, web content, video-on-demand, security and surveillance, fixed content, and reference data storage. |  |
| System Environment | Departmental and workgroup servers and workstations |  |
| Key RAID Features | Hot spares, RAID Level Migration, Online Capacity Expansion, Optimized Disk Utilization, and the following Adaptec Advanced Data Protection Suite features: Striped Mirror (RAID 1E) Hot Space (RAID 5EE) Dual Drive Failure Protection (RAID 6, 60) Copy back Hot Spare |  |
| Bus System Interface Type | PCI-X 64-bit/133 MHz host interface |  |
| External Connectors | One x 4 SAS connector For External SAS Host connection |  |
| Internal Connectors | Two x 4 SAS connectors |  |
| Data Transfer Rate | Up to 3Gb/s per port. |  |
| Features: Hot-Swap, Hot Spare and Redundant power. Supports RAID 6 RS-208 supports RAID 6 enhanced performance. RAID 6 is essentially an extension of RAID 5 which implements a second independent distributed parity scheme. RAID 6 can handle the failure of any two drives in the array while other single RAID levels can handle at most one fault. It provides the highest level ever of data protection without sacrifice the performance. Hot-Swap Drives & Redundant Hot-Swap Power supply SATA I/II, Serial Attached-SCSI (SAS) or Ultra 320 SCSI Disk Interface The next generation Hard disk drive (3Gbps performance) with features such as native command queuing (NCQ). Convenient Modularized Architecture R-STOR series is a fully modularized design that replaces all the cables with connectors. RAID Controller, cooling fans, disk drive, and power supply can be easily swapped to minimize the down time of the RAID service. EZSecur Lock, EZ swap or Replace Hard drive canisters The user-friendly drive tray/canister lock is designed with keyless and secure 2 steps safety measurement to prevent accidental removal of the hard drive. Smart Redundant fan & HDD Activity monitoring LED’s indicates if a drive is active, or failed. Striking the balance between thermal and acoustics, CePOINT’s smart redundant fan operates at a highly efficient cooling mechanism. The design of the 2 linear redundant fans in a module works more efficient to ventilate the heat out from the rear. |

Model RS-206 RS-208 RS-212 RAID Engine Intel Pentium X86 OR AMD Opteron/Athlon Controller# SATA-I/II ¦ SAS¦ SCSI (options in all the series) RAID Levels 0,1,5,6,,50,60,NRAID and JBOD Cache Support (Write back) Up to 2GB of 64-bit DDR 333 SDRAM System Type Rack mountable 2U Host Interface SAS or Fibre-Channel or Dual Ultra 320 SCSI Disk Interface SATA II ¦SAS¦ SCSI (options-all series) Host Transfer Rate 320MB/sec per channel No. of Disk Drives 6 8 12 Disk Activity/Failure LED Display Yes available in all the RS-models Hot Swap and redundant Yes (Power Supply, Hard Disk Drive & Fan) Hot Spare Yes Battery Back-Up Module Optional, Supporting 72 hours battery back-up time LAN Web browser-based RAID manager via build in 10/100 Ethernet port Array Management Support Yes. Automatic Bad-Sector & Error Recovery Yes. Automatic Drive Rebuilds Yes. Automatic Data rebuilds. Audible Alarm, Pager and Fax Notification Yes Remote Terminal Configuration Yes. Through RS-232 or 10/100 Ethernet port Operating Systems Windows XP/2000/2003, Linux, Unix, Sun Power Supply Redundant by Dual 375W Power modules with PFC feature, Loading Sharing type and cable-less design. Redundant by Dual 460W Power modules with PFC feature, Loading Sharing type and cable-less design. Electrical AC Voltage 110-230 VAC/AC Frequency 50-60Hz Temperature Operating Temperature : 10 to 35 degree C. Relative Humidity 20% to 80% non-condensing Dimensions 446.4(W) x 88.8(H) x 527(D) 446.4mm(W) x 132.4mm(H) x 482mm(D)

Cepoint  Networks, LLC. sales@cepoint.com  www.cepoint.com  Tel: 603-883-7979  Fax: (603)883-3266

Specifications subject to change without notice, All trademarks or registered trademarks are properties of their respective owners.