| One West Otterson Street, Nashua, New Hampshire 03060. Ph: (603)883-7979 Fax: (603)883-3266 Email: sales@cepoint.com Website: http://www.cepoint.com V1000NMS DIGITAL VIDEO OPTICAL TRANSMITTER / RECEIVER Overview The Product is a fiber optic digital multiplexer for transmitting 8 channel high quality, uncompressed digital video, 4 channels of bi-directional data and audio, 4 E1 and one 100M Ethernet over a single fiber cable. The product may also be maintained by our future product, V1000NMS, a Network Management System. Applications for this product include CCTV, video surveillance, homeland security, ITS and etc. Features |
| --- |
| Transports 8 channels of High quality video over one optical fiber cable Exceeds RS250C Medium Haul Specification for DG, DP and SNR. 8MHz video bandwidth, Compatible with NTSC, PAL and SECAM Uncompressed video, 8 Bit or 10Bit digital encoding/decoding Transmission of 4 channels of any directional audio Provides 4 channels of bi-dir data compatible with RS232, RS422/RS485 Supports 4 E1, G.703 standard One 10M/100M Ethernet compatible with IEEE802.3 Easy installation and adjustment free Transmission up to 60KM over one fiber Stand alone operation or mount in Model FB-CHS(FC-712-6) chassis Specifications |
| Power: 220VAC/50Hz, standalone device 0.6A@12VDC for card Indicators: Power, Optical Link Status Video Signal, Audio status, Data traffic E1 Alarm, Ethernet Link Status Video: Format: PAL/NTSC/SECAM Video Signal: 1Vp-p, 75ohm Digitization: 8bits/10bits Bandwidth: 8MHz DG <1% DP <1 degree SNR >65dB Connectors: 8 BNCs Audio Channel: 1~4, Bi-dir Audio Input: unbalanced, 600Ohms Digitization: 16bit@48k Frequency: 10Hz to 20KHz SNR: >70dB Connector: RJ45 | Data: Channel: 1~4, Bi-dir Data Rate: 0~~23.04Kbps/Ch Format: RS-232/RS-422/RS-485 Connector: RJ45 E1 support: Bit rate: 2.048Mb Line code: HDB3 Standard: ITU-T G.703 Connector: CC3(1.0/2.8) line impedance: 75ohm Jitter Performance: G.742 and G.823 Ethernet: Data Rate: 10/100Mbps auto detect Standard: IEEE802.3 Connector: RJ45 Auto-negotiation with half/full duplex Environment: Operating: -40oC~+70 oC Storage: -40oC~+85 oC Humidity: 0-95% Non-Condensing Physical Dimension: 176 x 220 x 50.8 (mm) card 180 x 237 x 55(mm) Standalone |
| Typical Pair Application Ordering Information Fiber Type Video Transmitter Video Receiver Range Notes Singlemode (09/125um) F7-8VT-W012F F7-8VR-W012F 40Km Video only F7-8VT-nATR-nDTR-W022F F7-8VR-nATR-nDTR-W022F 20Km F7-8VT-nATR-nDTR-100M4E1-042F F7-8VR-nATR-nDTR-100M4E1-042F 40Km Support 4E1, 100M Ethernet F7-8VT-nATR-nDTR-W042F F7-8VR-nATR-nDTR-W042F 40Km F7-8VT-nATR-nDTR-W062F F7-8VR-nATR-nDTR-W062F 60Km CWDM F7-8VT-WllllrrF2 F7-8VR-WllllrrF rrKm Video only F7-8VT-nATR-nDTR-WllllrrF3 F7-8VR-nATR-nDTR-WllllrrF rrKm Note: |
| Replace n within 1 through 4 for audio and data channel numbers Replace llll with CWDM wavelength, replace rr with requested distance Add -M at the end of model number for rack card product FC connectors standard, consult factory for other connectors. |

Contact:

Sales Department, Cepoint  Networks, LLC.  Phone (603)883-7979-Fax: (603)883-3266 E-mail: sales@cepoint.com http://www.cepoint.com